STEPS:

    1. Sort screws
    2. Use second and third link in dump to calibrate motors for the arm.
      The following code and be used:

#include <Servo.h>

Servo myservo; // create servo object to control a servo
// twelve servo objects can be created on most boards

int pos = 0; // variable to store the servo position

void setup() {
  myservo.attach(6); // attaches the servo on pin 9 to the servo object

 myservo.write(60); //this is where you set the initial angle
}

void loop() {

  for (pos = 60 ; pos <= 180; pos += 1) { // goes from 0 degrees to 180 degrees
    // in steps of 1 degree
    myservo.write(pos); // tell servo to go to position in variable 'pos'
    delay(15); // waits 15ms for the servo to reach the position
  }
  for (pos = 180; pos >= 60; pos -= 1) { // goes from 180 degrees to 0 degrees
    myservo.write(pos); // tell servo to go to position in variable 'pos'
    delay(15); // waits 15ms for the servo to reach the position
  }

}

This is the same code as 'sweep' in the servo templates.

    1. Use the second link in the dump to assemble the arm.
    2. Connect arm to breadboard and test that all motors work
    3. Discover the HEX codes for the signal sent from the IR Remote using the following code:
#include <IRremote.h>
int RECV_PIN = 11;
IRrecv irrecv(RECV_PIN);
decode_results results;

void setup()
{
  Serial.begin(9600);
  irrecv.enableIRIn(); // Start the receiver
}

void loop()
{
  if (irrecv.decode(&results))
    {
     Serial.println(results.value, HEX);
     irrecv.resume(); // Receive the next value
  }
}
1. After the HEX codes are found, verify they are the same to the provided remote control sketch. Change all non-corresponding values.
2. Test to make sure that when a button is pressed on the remote that a function is called
3. Connect the IR sensor and arm to the same breadboard and Arduino.
4. Test to make sure that every function moves the arm in some way. It is set to move one degree at a time so be patient.